## Slide 1
Aerosol profiling by ground-based, airborne and spaceborne lidar systems: working principles, highlights, and perspectives
Dr. Lucia Mona
CNR-IMAA
Italy

## Slide 2
Aerosols: what is and why is relevant
Profiling needs
Aerosol lidar techniques
Example of aerosol lidar measurements
Products
Current lidar observations
What next?
OUTLINE

## Slide 3
Aerosol: is a suspension of fine solid particles or liquid droplets in air (Wikipedia)
Highly variable in space time and composition
Health
Some types related to small particles and certain compositions have larger impacts
Air quality
PM10 and PM2.5 are air quality indicators.
Aerosol and its impacts

## Slide 4
Aerosol and its impacts
Climate change
Absorbing aerosols have a positive impact, while reflecting ones reduce the effects of greenhouse gases. Indirect effect still uncertain.
Precipitations
Depending on size and shape, aerosol can be more effective for occurrences of strong events

## Slide 5
PM10
PM2,5
PM1
Sulfate
Ammonium
Nitrate
Chloride
Organic matter
Brown/black carbon
OC/EC
VOC
Particle size distribution
Measurements at the surface

## Slide 6
Profiling: why important?
Buondary Layer
From surface to UTLS different interactions, effects and impacts

## Slide 7
Profiling: why important?
Aerosol
Strong impact on radiation budget for UTLS layers
Impact on aviation
Long range transport in the Free troposphere
Impact on radiation budget for lofted layers
Formation of clouds and precipitations in the Free troposphere
air quality & health in the PBL
impacts on agriculture and environment at the surface

## Slide 8
Elastic Lidar
Aerosol lidar: basic equations
2 unknows to be solved assumption needed about a/b
which means assumption on type of particle
Example of only-elastic lidars: ceilometers, CALIOP
Signal collected at the laser wavelength
PRO:
less expansive
same capability day and night
CONS:
Strong assumption needed
Highly sensitive to calibration procedure

## Slide 9
Raman lidar
Aerosol lidar: basic equations
Signal collected at a wavelength shifted respect to laser wavelength
Shift depending on the target molecules in the atmosphere
d = Angstrom coefficient
a=coeff l-d
p=particles
g=gases

## Slide 10
Aerosol lidar: basic equations
Raman signal
Known through the extinction
PRO:
More accurate
Provides info about aerosol type
CONS:
Low signal-to-noise ratio
Extinction efficiently determined only in night-time
Elastic signal
Backscatter retrievable with no significant assumptions

## Slide 11
High Spectral Resolution Lidar
PRO:
Good signal to noise ratio
CONS:
instrumental complexity
HSRL utilizes high-spectral-resolution optical filters to resolve the Doppler-broadened molecular scattering spectrum and the aerosol signal
Two main set up possiiblities
Fabry-Perot etalon (less stable)
robust and stable atomic/molecular absorption filter (available only at some wavelengths)

## Slide 12
Particle depolarization ratio
NOTES
Easy to be implemented
Accurate calibration methods required (Freudenthaler, et al. Tellus B,2009)
The way in which particles in atmosphere modify the polarization status of the emitted laser beam (and its return) is related to asphericity of the particles:
the more they depolarize, the more aspherical they are
The particle depolarization ratio d can be measured using depolarizing cube separating the perpendicular depolarized component of the backscattered radiation

## Slide 13
Example of aerosol lidar observations
Aerosol lidar measurements @ 1064 nm CNR-Potenza-IT
Interface PBL- free troposphere
Intense layer of desert dust
Feeble aerosol layer
Thin cirrus

## Slide 14
Potenza, Lidar
AOD@532 nm = 0.30 (in the dust layer = 0.25)
AOD@355 nm = 0.33 (in the dust layer = 0.25)
Mean values in the layers
Columnar integrated quantities (like AOD)
Layer integrated quantities (like AOD)
Layer typing
Dust back and ext
Dust concentration
Fine and mode concentration
Example of aerosol lidar observations

## Slide 15
Dust extinction profiles
d
b
bdust
adust
Freudenthaler et al., 2009
Tesche et al., 2009
Papagiannopolus et al., 2009
EARLINET profile measured at Potenza lidar station on 22nd May 2014

## Slide 16
Microphysical retrieveals
Multiwavelength measurements including extinction, backscatter and depolarization can allow, through specific advanced inversion algorithms, the retrieval of micrphysical properties like:
Number concentration
Effective radius
Volume concentration
Refractive index
Muller, et al. Applied Optics,2019

## Slide 17
Microphysical retrieveals
In order to make an assessment of this comparison with in situ measurement is needed.
This is an example with HSRL on aircraft vs colocated in situ measurements
Muller, et al. Applied Optics,2019

## Slide 18
Microphysical retrieveals
More methods and algorithms have been developed.
Some papers about
Böckmann, C.: Appl. Optics, 2001.
Böckmann, C., et al., J. Opt. Soc. Am. A, 2005.
Müller, D., et al., Appl. Optics, 1998.
Müller, D., et al., Appl. Optics, 1999.
Müller, D., et al., Atmos. Meas. Tech2014.
Müller, D., et al., Atmos. Meas. Tech., 2016.
Veselovskii, et al., Appl. Optics, 2002.
Veselovskii, I., et al.,, Atmos. Meas. Tech., 2013.
Veselovskii, I., Atmos. Chem. Phys., 2016.

## Slide 19
Combined lidar and photometer products
Photometer provides columnar Aerosol Optical Depth at different wavelengths and, through retrievals, size distribution , single scattering albedo , fine/coarse fraction.
AERONET
An example for 24 June 2022, Bejing

## Slide 20
Combined lidar and photometer products
Synergy of profiling and columnar info allows for more robust retrievals and determination of constrained concentration profiles in fast and automatic way.
LIRIC (LIdar-Radiometer Inversion Code)
GARRLiC (Generalized Aerosol Retrieval from Radiometer and Lidar Combined data)
Bovchaliuk, et al. Atm. Meas. Tech.,2016
RR= lidar only inversion
NNMB/BSC dust forecast

## Slide 21
Knowing the type of the aerosol can help to:
understand sources, transformations, effects, and feedback mechanisms
improve accuracy of satellite retrievals and aerosol models
quantify assessments of aerosol radiative impacts on climate
investigate the impact of the different aerosol sources on climate, precipitation and air quality.
improve the aerosol emissions policies
define actions for local authorities and hazards management
Aerosol typing: why important?

## Slide 22
Total AOD
Dust
Sea salt
Biomass Burning
Sulphate
Forecast 15 May 2021 03 UTC
http://atmopsphere. copernicus.eu
Aerosol typing: CAMS example
Copernicus Atmospheric Monitoring System

## Slide 23: How to know about aerosol types The general approach
Identify the source for defining the aerosol characteristics
Investigate characteristics for understanding the source
More common in Ground Based observations
More common in satellite observations
Inputs for defining automatic procedures for typing
Measurements
Sources
Procedures

## Slide 24
+
OPAC + RH,
GDAC microphysics
Mischenko spheroidal model
Linear mixing of different components
Nicolae et al., ACP 2018
Aerosol typing: MW Raman – HSRL feature
NATALI
Neural network Aerosol Typing Algorithm based on aerosol LIdar data

## Slide 25
Burton et al., AMT 2012
Aerosol typing : HSRL airborne
Mahanalobis distance typing method based on NASA Langley Research Center (LaRC) airborne HSRL obs

## Slide 26: More tiny the classification higher its reliability
Dust & dusty mixture
Absorbing particles
Clean continental
Mixed marine
Dust
Polluted dust
Mixed dust
Absorbing particles
Clean continental
Mixed marine
Dust
Polluted dust
Mixed dust
Polluted continental
Smoke
Clean continental
Mixed marine
4 classes
6 classes
7 classes
Improving insight
Improving typing reliability
Backscatter Angstrom 355/1064 nm + Lidar Ratio at 355nm
+ Ratio of lidar ratio 355/532 nm
Papagiannopoulus et al., ACP 2018

## Slide 27
Method observation-only based (Nicolae et al., 2018)
Results for low troposphere , nighttime obs, 2015-2020
Continental ContinentalPolluted Dust Mineral mixture Marine/CC Smoke
Example on long term observations
Courtesy of Doina Nicolae – EARLINET/ACTRIS

## Slide 28
Aerosol typing: CALIPSO example

## Slide 29
Different types provided… but how it works?
Aerosol typing: CALIPSO example

## Slide 30
CALIPSO is a backscatter lidar
Basic equation has 2 unknowns: aerosol extinction and aerosol backscatter
CALIPSO to solve it assumes the extinction/backscatter ratio time by time altitude by altitude
HOW?
Look up table on the base of aerosol typing
So the products (extinction and backscatter) are the result of the typing scheme
CALIPSO typing based on assumptions and needed for retrievals
Aerosol typing: CALIPSO example

## Slide 31
Profiling networks: aerosol lidar
GALION
(GAW Aerosol LIdar Observational Network)
AD-NET
ALINE
CISLINET EARLINET MPLNET
NDACC
REALM
Network of regional networks
Cooperation and harmonization are fostered
https://community.wmo.int/activity-areas/gaw

## Slide 32
Profiling networks: aerosol lidar

## Slide 33
MPLnet:
US+Asia- elastic lidar + photometer Operational h24/7d
LALINET:
South America, few sites, in connection with EARLINET and Adnet for developments, Raman and elastic lidars
EARLINET:
Europe - multiwavelength Raman with depolarization Pre-Operational, typically colocated photometer Long Term funds
AD-net:
Asia, 3b+2a+2d lidars, operational 24h /7d
Eprofile:
low power elastic lidar, high dense distribution, fully operational h24/7d
Profiling networks: aerosol lidar

## Slide 34
Satellite aerosol lidars
Currently flying aerosol lidars
CALIOP on CALIPSO since 2006
ADM Aeolus since2018
ATLID on EarthCARE 2023
Providing data in NRT for wind but even about aerosol within identified aerosol layers
EarthCARE
ESA Earth Cloud, Aerosol and Radiation Explorer mission
HSRL + depol at 355 nm
First ever spaceborne lidar providing independent extinction and backscartetr coefficients

## Slide 35
What next?
Hot topics:
Aerosol and clouds investigations
Aerosol and RH
Aerosol and wind
Profiling and in situ combined for better insight
Bioaerosol
New technical challenges
Mobile systems measuring while moving
Cheep lidar for remote poor areas investigation

## Slide 36
THANK YOU
lucia.mona@imaa.cnr.it