## Slide 1: Development of Micro Pulse Lidar Network (MPLNET) Level 3 Satellite Validation Products in Advance of the EarthCARE Mission
Jasper R. Lewis1, James R. Campbell2, Simone Lolli3, Sebastian A. Stewart4, Larry R. Belcher4, Rob Koopman5, Michaël Sicard6, Erica Dolinar2, Stephanie Rusli5, Jason Tackett7, Ellsworth J. Welton8
1 University of Maryland Baltimore County, GESTAR II, Baltimore, MD, USA, jasper.r.lewis@nasa.gov
2 Naval Research Laboratory, Monterey, CA, USA, james.campbell@nrlmry.navy.mil, erica.dolinar.ctr@nrlmry.navy.mil
3 Italian National Research Council (CNR), IMAA, Tito Scalo (PZ), Italy, simone.lolli@cnr.it
4 Science Systems and Applications Inc., Greenbelt, MD, USA, sebastian.a.stewart@nasa.gov, larry.r.belcher@nasa.gov
5 European Space Agency (ESA/ESTEC), Noordwijk, Netherlands, Rob.Koopman@esa.int, Stephanie.Rusli@esa.int
6 Universitat Politècnica de Catalunya, Barcelona, Spain, michael.sicard@upc.edu
7 NASA Langley Research Center, Hampton, VA, USA, jason.l.tackett@nasa.gov
8 NASA Goddard Space Flight Center, Greenbelt, MD, USA, ellsworth.j.welton@nasa.gov

## Slide 2: Development of Micro Pulse Lidar Network (MPLNET) Level 3 Satellite Validation Products in Advance of the EarthCARE Mission
EarthCARE
Satellite (2023 launch)
Wavelength: 355-nm
Pulse energy: 38 mJ
Repetition rate: 51 Hz
Telescope: 62 cm
FOV: 65 mrad
Vertical resolution: 100 m, below 20 km
Horizontal resolution: 282 m
MPLNET
Surface-based network
Wavelength: 532-nm
Pulse energy: 6 – 8 mJ
Repetition rate: 2500 Hz
Telescope: 18 cm
FOV: 100 mrad
Vertical resolution: 75 m
Continuous, 24/7 observations
CALIPSO
Satellite
Wavelengths: 532-nm, 1064-nm
Pulse energy: 110 mJ
Repetition rate: 20.25 Hz
Telescope: 100 cm
FOV: 130 mrad
Vertical resolution: 60 m, 8.2 to 20.2 km 30 m, below 8.2 km
Horizontal resolution: 333 m

## Slide 3: We Utilize Two Validation Products
Level 3 (L3) MPLNET Products
  Full 24-hour diurnal cycle
  Derived from hourly means of the quality screened L2 (L15) products
Level 3 Satellite Validation Products
  Same process as L3 but constrained to satellite overpass times (e.g. L3-CAL for CALIPSO)
  Within ±2 hours and 200 km of MPLNET site
Figures show NRB and observed minutes for GSFC site (Greenbelt, MD) 2019 – 2021
  L3: 34 months (1016 days)
  L3-CAL: 34 months (228 days)
  Vertical dashed lines indicate mean CALIPSO overpass times
L3 NRB
L3 NRB
UTC
L3-CAL NRB
L3-CAL NRB
(Night)
(Day)
~17% decrease

## Slide 4: Cloud Comparison
Vertical cloud fractions for MPLNET L3 CLD and L3-CAL CLD are calculated using a 1-km by 1-hr grid
CALIOP cloud fractions are calculated from the Level 2, 5 km Vertical Feature Mask and a vertical resolution of 1 km (CAD > 20)
Figures show L3 and L3-CAL cloud fractions for GSFC (2019 – 2021) and comparisons to CALIOP cloud fractions for daytime and nighttime observations
UTC
Range (km)
L3 CLD
L3-CAL CLD
Range (km)
Cloud fraction
Cloud fraction
0.00
Range (km)
Night
Day
Cloud fraction
Cloud fraction

## Slide 5: Aerosol and PBL Comparisons
Aerosol fraction
Aerosol fraction
MPLNET aerosol fraction follows same procedure as the cloud fraction
  L3: 34 months (1001 days)
  L3-CAL: 31 months (205 days)
CALIOP AOD and extinction profile come from the Version 4 L3 tropospheric aerosol profile (cloud free)
CALIOP mixed layer top uses the first surface-attached (within 200 m) aerosol layer from the L2 5-km merged layer product (daytime only)
Altitude (km)
Night
Day
Extinction (km-1)
Extinction (km-1)
L3 AER
L3-CAL AER
UTC
UTC

## Slide 6: Some of Our Ongoing Work
Fall (SON)
Winter (DJF)
Spring (MAM)
Summer (JJA)
Investigating seasonal changes in the L3 products and
how they impact MPLNET/satellite comparisons
Utilizing multiyear records of MPLNET data at sites around the globe
Barcelona (Spring 2022)
Active
Inactive

## Slide 7: Take Home Messages
In advance of future satellite missions (e.g. EarthCARE and AtmOS) we are developing two flavors of Level 3 (L3) MPLNET products to facilitate satellite-MPLNET validation and analysis. This work will also benefit future modeling studies.
Preliminary MPLNET/CALIOP comparisons at GSFC show:
  Similar bimodal cloud fraction distribution, though they differ in the cloud amount (higher amounts of cirrus seen from CALIOP)
  Aerosol extinction and AOD show better agreement at nighttime than daytime
  Mixed layer heights are in good agreement
We will also examine seasonal and regional comparisons using multi-year datasets available from CALIPSO and MPLNET in order to develop a standard operating procedure to be implemented during the EarthCARE mission.
Acknowledgements: This research was supported by the Earth Science U.S. Participating Investigator Program NASA Grant Number 80NSSC21K0560. The NASA Micro Pulse Lidar Network is funded by the NASA Earth Observing System and the NASA Radiation Sciences Program. CALIPSO data were obtained from the NASA Langley Research Center Atmospheric Science Data Center.